Easy Step By Step Touch Monitor Installation Instructions

    Tools you may need: small knife or scissors, 1 small screwdriver, 1 medium
    sized Philips head screwdriver, and possibly 1 medium sized regular (pan
    head) screwdriver, and a couple pieces of tape.

    1. Carefully remove your new touch monitor from the box. Save the box and
    all the packing: you'll use it to ship your old monitor back to Club Data.

    2. Carefully remove all plastic wrapping. Be careful not to cut any of the
    cables coming out of the back of the monitor! Inspect the case and screen
    -- make sure no damage occurred from shipping. Attach the swivel base -- it
    snaps in place.

    3. Make sure your computer is powered OFF, BUT LEAVE IT PLUGGED INTO THE
    WALL! With a screwdriver, detach your old monitor from the computer. Make
    note of the connectors into which the monitor was plugged. IMPORTANT: Mark
    these with pieces of tape so you'll remember where it was plugged in.
    Unplug the power cord from the back of the monitor. (The old power cord
    will work with the new monitor so you don't have to replace it unless you
    want to. A new power cord came with the new monitor.)

    4. Remove the screws in the back of the computer case to remove the cover.
    These screws are normally found in each corner of the back and possibly one
    near the middle top of the computer's back side. Set these aside for now.

    5. CAREFULLY, slide the cover off the computer. Sometimes they fit snugly,
    and you may have to wiggle it a little to loosen it. Don't knock or hit it!
    Remove the cover completely and set it aside.

    6. Inside along the back side of the computer are several interface "cards"
    which help make the computer work. Your old touch monitor was plugged into
    two of them. You need to remove the mounting screws which hold these two
    cards in (at the very back edge of the card against the back of the
    computer). Save these screws. Then firmly (but carefully!) grasp one card
    at a time and lift it out of its slot. They fit snugly, so you may have to
    wiggle the card a bit from front to back (not sideways!) to loosen it. Put
    each of the cards in one of the bubble wrap pouches we sent you and wrap it
    with a rubber band. Set both aside for now -- you'll be shipping these back
    to us with the old monitor.

    7. Into one of the slots where a card was, insert the new VGA card. Make
    sure it goes all the way in. Replace the mounting screw.

    8. Into the slot from which you removed the other card, insert the spare
    slot cover. It's important to cover all the slots so the computer gets
    proper cross ventilation inside when the cover is on. Again, use the
    mounting screw to secure the slot cover.

    9. Carefully slide the computer case back on. Be careful not to catch the
    case on any wires or cables -- sometimes there are a lot of them! Just tuck
    them down carefully and slide the cover back on. Then replace the cover
    screws again.

    10. Plug your new touch monitor into the power cord.

    11. Plug the monitor's VGA plug into the new VGA card you installed. The
    VGA plug is the larger one which has about a dozen little gold pins inside
    the plug. Be careful to plug it straight in, and then lightly twist the
    screw mounts on each side of the plug.

    12. Plug the other monitor cable (a longer, thinner one with a plug which
    has 9 holes in the end) into one of the computer's back connectors which
    accepts the plug. You can tighten the small plug screws to keep it firmly
    attached for now, too.

    13. Turn on the computer and monitor. You should see your startup menu
    appear.

    14. Get to the DOS prompt (if you use our menu system, type an asterisk to
    drop to the DOS level). You should see something like C:> or D:> on the
    screen.

    15. Insert the Microcal diskette in drive A: and type A: to log the
    diskette. The software on the disk is used to calibrate the touch monitor
    so it will talk to your Touch-N-Sell software. You can do one of two things
    with the disk: you can run the software directly from the diskette or you
    can install the Microcal software on your hard disk. Type INSTALL for more
    information on installing the software on your hard disk. FOR NOW, let's
    run the software directly from the diskette.

    16. With the A:> prompt on the screen, type MICROCAL to start the program.
        Then press the SPACE bar to get the main menu screen.

    17. Use the UP/DOWN arrow keys to highlight DIAGNOSTICS; press <ENTER>.

    18. Highlight FIND TOUCH SCREEN; press <ENTER>.

    19. Highlight SERIAL; press <ENTER>. If it finds the touch screen, it will
    beep and display information on the right side of the screen in the STATUS
    window. Write down what it says for PORT, BAUD and PARAMETERS.

    20. If these settings are COM1, 4800 baud, and N72, that's good! Go to
    step #21 below. OTHERWISE....

        a) If it says COM2, it can probably work fine except if your receipt
           printer is set to print to COM2, you'll have a conflict. The touch
           monitor and receipt printer COM ports must be unique. Suggestion:
           move the receipt printer to COM2 and plug the monitor into COM1.
           Then in the TNS SETUP module, you'll have to tell the system to
           print receipts to the proper COM port for the receipt printer.

        b) If it says 9600, we need to run MICROCAL again to FORCE the
           monitor to 4800 baud. Here's how:
               (1) Start MICROCAL again from the floppy disk.
               (2) Have it "find" the touch screen again as explained in steps
                   17-19 above.
               (3) Highlight CALIBRATION and press <ENTER>. Touch the screen
                   where indicated.
               (4) Highlight CONFIGURE and press <ENTER>.
               (5) Highlight AUTO BAUD DETECTION ENABLE and press <ENTER>
               (6) Highlight 4800 and press <ENTER>
               (7) Then highlight selections to EXIT, all the way to exit the
                   program.

    21. Now from the C:\ prompt, type CALIB to calibrate the screen for
    Touch-N-Sell. It should work.

    22. Lastly (sigh!) you need to check the batch files which start your
    Touch-N-Sell system to make sure they set the COM ports to the proper
    communications settings. Check the TNS.BAT file in the C:\ root directory.
    Assuming that the touch monitor is plugged into COM1 and the receipt
    printer is in COM2, here's what you'd want to find in the TNS.BAT file:
                        MODE COM1:4800,N,7,2
                        MODE COM2:9600,E,7,2
    Make whatever edits you need to effect the changes.

    23. Now comes the fine print. It's possible that by installing the touch
    monitor, you may lose your report printer (temporarily) because some old
    CGA monitor cards also included a parallel printer port. When you replace
    such a CGA video card with a VGA card, you lose the printer port because
    VGA cards don't have a printer port built into them. And depending on what
    other interface cards you have installed, you may or may not need to add a
    parallel printer card to get your parallel report printer working again.
    Here's where you need to call us if you find extra cables that used to plug
    into the back of your computer but which now don't have a home!